## Slide 1: LT9611UXC --- Product Brief Dual-Port MIPI DSI/CSI to HDMI2.0 with Audio
LT9611UXC ADVANCE INFORMATION – CONFIDENTIAL AND PROPRIETARY
Features
Single/Dual-Port MIPI DSI/CSI Receiver
  Compliant with D-PHY1.2 & DSI1.3 & CSI-2 1.3
  Integrated DSC1.2 decoder
  1/2 configurable ports
  1 clock lane and 1/2/3/4 configurable data lanes per port
  80Mbps~2Gbps per data lane
  Skew calibration
  Programmable receiver equalizer
  Support data lane swap(arbitrarily) and polarity inversion(independent)
  3D support: two ports simultaneously receiving L and R frames or odd-L/even-R alternative pixels
  DSI support both burst mode and non-burst mode
  DSI support video formats:
DSC/CSC disabled: Packed 16/18/24/30/36-bit RGB, Loosely Packed 18-bit RGB, Packed 16/24-bit YCbCr4:2:2, Loosely Packed 20-bit YCbCr4:2:2, Packed 12-bit YCbCr4:2:0
DSC disabled, CSC enabled: Packed
16/18/24/30/36-bit RGB, Loosely Packed 18-bit RGB, Packed 16/24-bit YCbCr4:2:2, Loosely Packed 20-bit YCbCr4:2:2
DSC enabled, CSC disabled: Packed 24-bit RGB, Packed 16-bit YCbCr4:2:2, Packed 12-bit YCbCr4:2:0 DSC/CSC enabled: Packed 24-bit RGB, Packed 16-bit YCbCr4:2:2
  CSI support video formats:
DSC/CSC disabled: RGB565/666/888, YUV422
8/10-bit, Legacy YUV420 8-bit
DSC disabled, CSC enabled: RGB565/666/888, YUV422 8/10-bit
DSC enabled, CSC disabled: RGB888, YUV422 8-bit,
Legacy YUV420 8-bit
DSC/CSC enabled: RGB888, YUV422 8-bit
Digital Audio Input
  I2S interface supporting 2-channel audio, with sample rates of 32~192 kHz and sample sizes of 16~24 bits
  SPDIF interface supporting PCM, Dolby Digital, DTS digital audio at up to 192kHz frame rate
  IEC60958 or IEC61937 compatible
HDMI2.0 Transmitter
  Compliant with HDMI2.0b, HDMI1.4 and DVI1.0
  Compliant with HDCP2.2 and HDCP1.4
  Data rate up to 6Gbps
  On-die back termination
  Programmable transmitter swing and pre-emphasis
  AC-couple capable
  Support channel swap(arbitrarily) and polarity inversion(independent)
  Support 4k@60Hz
  Supported 3D formats: side-by-side(full)
  Supported video formats:
DSC/CSC disabled: 24/30/36-bit RGB, 16/20/24-bit YCbCr4:2:2, 8-bit YCbCr4:2:0
DSC disabled, CSC enabled: 24-bit RGB/YCbCr4:4:4, 16-bit YCbCr4:2:2
DSC enabled, CSC disabled: 24-bit RGB, 16-bit YCbCr4:2:2, 8-bit YCbCr4:2:0
DSC/CSC enabled: 24-bit RGB/YCbCr4:4:4, 16-bit YCbCr4:2:2
  HDR support
  Support TMDS scrambling for EMI/RFI reduction
  Support SCDC
  5V tolerance DDC/HPD I/Os
Miscellaneous
  CSC: RGB <-> YUV444 <-> YUV422
  Integrated CEC Controller
www.lontiumsemi.com

## Slide 2
LT9611UXC ADVANCE INFORMATION – CONFIDENTIAL AND PROPRIETARY
External oscillator
Integrated microprocessor
Embedded SPI flash for firmware and HDCP keys
GPIOs for system controls
Integrated 100/400kHz I2C slave
Firmware update through SPI or I2C interface
Power supply: 3.3V for I/O and 1.2V for core
ESD 4kV HBM
Temperature Range: -40℃ ~ +85℃
Package: QFN64 (7.5mm*7.5mm)
Description
The LT9611UXC is a high performance MIPI DSI/CSI to HDMI2.0 converter for STB, DVD applications.
The MIPI DSI/CSI input features configurable single-port or dual-port with 1 high-speed clock lane, and 1~4 high-speed data lanes operating at maximum 2Gbps/lane, which can support a total bandwidth of up
to 16Gbps. LT9611UXC supports burst mode DSI video data transferring, also supports flexible video data mapping path. Integrated DSC decoder implements up to 1:3 visually lossless decompression which reduces bandwidth requirement for UHD video transport, also power consumption and EMI.
The HDMI2.0 output supports data rate up to 6Gbps which provides sufficient bandwidth for 4k@60Hz video. Also HDCP2.2 is supported for data encryption.
Two digital audio input interfaces are available, I2S and SPDIF. The I2S interface supports 2-ch LPCM and the SPDIF interface supports 8-ch LPCM or compressed audio, both at maximum 192kHz sample rate.
The device is capable of automatic operation which is
enabled by an integrated microprocessor that uses an embedded SPI flash for firmware storage. System control is also available through the configuration I2C slave interface.
Applications
STB
DVD/BD
PTV Box
Figure1. Application Diagram
Ordering Information
Part Number | Operating Temperature Range | Package | Packing Method
LT9611UXC | -40℃ to +85℃ | QFN64 (7.5*7.5) | Tray
www.lontiumsemi.com

## Slide 3
LT9611UXC ADVANCE INFORMATION – CONFIDENTIAL AND PROPRIETARY
Copyright © 2016-2017 Lontium Semiconductor Corporation, All rights reserved.
Lontium Semiconductor Proprietary & Confidential
This document and the information it contains belong to Lontium Semiconductor. Any review, use, dissemination, distribution or copying of this document or its information outside the scope of a signed agreement with Lontium is strictly prohibited.
LONTIUM DISCLAIMS ALL WARRANTIES, EXPRESSED OR IMPLIED, INCLUDING THOSE OF NONINFRINGEMENT, MERCHANTABILITY, TITLE AND FITNESS FOR A PARTICULAR PURPOSE. CUSTOMERS EXPRESSLY ASSUME THEIR OWN RISH IN RELYING ON THIS DOCUMENT.
LONTIUM PRODUCTS ARE NOT DESIGNED OR INTENDED FOR USE IN LIFE SUPPORT APPLIANCES, DEVICES OR SYSTEMS WHERE A MALFUNCTION OF A LONTIUM DEVICE COULD RESULT IN A PERSONAL INJURY OR LOSS OF LIFE.
Lontium assumes no responsibility for any errors in this document, and makes no commitment to update the information contained herein. Lontium reserves the right to change or discontinue this document and the products it describes at any time, without notice. Other than as set forth in a separate, signed, written agreement, Lontium grants the user of this document no right, title or interest in the document, the information it contains or the intellectual property in embodies.
Trademarks Lontium™ 龙迅™ and ClearEdge™ is a registered trademark of Lontium Semiconductor. All Other brand names, product names, trademarks, and registered trademarks contained herein are the property of their respective owners.
Visit our corporate web page at: www.lontiumsemi.com Technical support: support@lontium.com
Sales: sales@lontium.com
www.lontiumsemi.com